## Slide 1: Machine Learning Image Based Pest Species Identification For Embedded Systems
SFSU ENGR 859 Spring 2024
Joshua Mehlman, SFSU ID #903035606, JMehlman@sfsu.edu

## Slide 2: Gather Initial Image
Trigger On Motion to Capture Initial Dataset
  Save the largest image we can as a JPEG
  Use Image Diff to find motion on smaller BITMAPS
    Subtract the R, G, and B from each prior to each image.
  asdf
Did not work so well. Branch motion was too much to sort.
I should probably use some sort of Machine Learning to find the objects…
  Capture a lot of images and manually tag.

## Slide 3: Get Working on Device
Start with super tiny leNet model to find out how large of image size we can handle.
  Initial model size ~50kB
    Still: 3M (At JPG Qual 70)
    Video: 640x480
Notes: The library has demons!
No, not damons, deamons!

## Slide 4: Start Over With Arduino Library
Start with super tiny leNet model to find out how large of image size we can handle.
  Initial model size ~50kB
    Still: 640x 480 (VGA)
    Video: 320x240 (QVGA)
    Smallest image size is: 96x96
  Max model size:
    Camera Memor:1.5 MB
    Image Size at QVGA: 153.6kB
Notes: There is no way a 96x96 image will work.
This is called “Foreshadowing”

## Slide 5: Model Wont Build
The Sony Spresense TFLite Build has no logging.
  MIC to the rescue: The MIC Spresense TFLite Build Shows what is missing

## Slide 6: We have Pipeline: Now Build Model
Ok, we do not have enough time left for SSD or Yolo.
Start with a full sized leNetV5
  Model Size = 480kB
Image size:
  Video Stream:
  Stills:
Notes: Crap!

## Slide 7: Use Pre-Trained Model
Start with a pretrained model
Prune
Model List:
Asdf
Notes: Ok, new plan

## Slide 8: No Way It Will Work on Full Image
Have to go to 96x96 images to fit…
  That is small <show image>
Crop, not scale
  The Spresense Camera Arduino library Can only zoom with:
    CAM_IMAGE_PIX_FMT_YUV422
  Fun Fact: The only errors the camera seems to know is:
    return CAM_ERR_INVALID_PARAM;
    return CAM_ERR_NO_MEMORY;
Notes: Guess how long that took to find out?
Sony documentation at is best
I saw both of these errors quite a lot

## Slide 9: Not Enough Images (Too Many Empty)
Augment: Every Squirrel and Bird gets:
  Permute
  Rotate

## Slide 10: Full Pipeline Aceved!
Capture Images
Tag Images
Train Model
Export Model
Install on Device
Run model!

## Slide 11: Run Real data (AKA: And My Troubles Began)
Now that we have a Pipeline

## Slide 12: Pruned Pre-Trained Model
Pruning a modern… back connected see slide
Notes: Thanks for the help on that Mr Lin

## Slide 13: It Works!
Time train for real.
  Gather All the images. Set the model to save when it has a squirrel or a bird
  Manually tag, using false positives in the “Empty” set
Switch to a faster MobileNetV5
Iterate on the training and Hyperperamiters

## Slide 14: New Plan: Run With What I Have
Performance is remarkably good!

## Slide 15: Results
Comair speed to Mr Lin